## Slide 1: Lead and Copper Update
Braintree Department of Public Works

## Slide 2: Introduction
Environmental Protection Agency (EPA) Lead and Copper Rule revisions took effect on October 16, 2024.
Requirements of the revisions:
  Develop a town-wide water service inventory
  Notify, via US Mail, all residences that have lead water services, galvanized iron water services, or water services of unknown material
  Within 3 years, develop a long-term action plan to eliminate lead from the water system
Informational Material available on BWSD website and by phone

## Slide 3: Braintree Lead and Copper History
1991
Lead and Copper Rule goes into effect

## Slide 4: Braintree Lead and Copper History
1991
Lead and Copper Rule goes into effect
2002
Braintree Optimizes Corrosion Control Treatment utilizing Sodium Hydroxide to adjust pH and a blended Ortho/Poly Phosphate to form a protective coating on the inside of the piping

## Slide 5: Braintree Lead and Copper History
1991
Lead and Copper Rule goes into effect
2002
Braintree Optimizes Corrosion Control Treatment utilizing Sodium Hydroxide to adjust pH and a blended Ortho/Poly Phosphate to form a protective coating on the inside of the piping
2020
Filter media changed for the Treatment of PFAS, triggering more frequent testing for lead and copper. Town required to sample 60 sites twice a year.

## Slide 6: Braintree Lead and Copper History
1991
Lead and Copper Rule goes into effect
2002
Braintree Optimizes Corrosion Control Treatment utilizing Sodium Hydroxide to adjust pH and a blended Ortho/Poly Phosphate to form a protective coating on the inside of the piping
2020
2024
Filter media changed for the Treatment of PFAS, triggering more frequent testing for lead and copper. Town required to sample 60 sites twice a year.
Monitoring Frequency Reduced to 30 Samples. Braintree still in compliance

## Slide 7: Braintree Sample Protocols
Daily
Water Quality Parameters are checked on a daily basis on the Finished Water. Adjustments in treatment are made to ensure that target doses are maintained

## Slide 8: Braintree Sample Protocols
Daily
Water Quality Parameters are checked on a daily basis on the Finished Water. Adjustments in treatment are made to ensure that target doses are maintained
Monthly
Water Quality Parameters are checked at our bacteria sites throughout the Town. Results will determine if the target dosages need to be changed at the Treatment Plant

## Slide 9: Braintree Sample Protocols
Daily
Water Quality Parameters are checked on a daily basis on the Finished Water. Adjustments in treatment are made to ensure that target doses are maintained
Monthly
Water Quality Parameters are checked at our bacteria sites throughout the Town. Results will determine if the target dosages need to be changed at the Treatment Plant
Yearly
30 Sites that were selected by the Town and approved by the DEP are sampled for lead and copper. Also, two schools are sampled and rotated for compliance. The School Dept has also tested for lead and copper at all the schools independently.

## Slide 10: What can Residents Do? Ways to Reduce Lead in Drinking Water
Let your water run until it gets to its coldest temperature (10-15 seconds). This ensures that you are pulling water from the water main in the street where there is no lead. Water has to be in contact with lead for a minimum of 6 hours in order for the leeching of lead to occur.

## Slide 11: Ways to Reduce Lead in Drinking Water
Let your water run until it gets to its coldest temperature (10-15 seconds). This ensures that you are pulling water from the water main in the street where there is no lead. Water has to be in contact with lead for a minimum of 6 hours in order for the leeching of lead to occur.
Use a point of use filter for drinking. Lead cannot be absorbed through the skin and has to be consumed in order to be a health risk. A point of use filter will filter out lead and give you peace of mind. These filters usually last 6 months under normal use.

## Slide 12: Ways to Reduce Lead in Drinking Water
Let your water run until it gets to its coldest temperature (10-15 seconds). This ensures that you are pulling water from the water main in the street where there is no lead. Water has to be in contact with lead for a minimum of 6 hours in order for the leeching of lead to occur.
Use a point of use filter for drinking. Lead cannot be absorbed through the skin and has to be consumed in order to be a health risk. A point of use filter will filter out lead and give you peace of mind. These filters usually last 6 months under normal use.
Replace your Service Line. Your service line is made up of two sections. From the Water main to the property line is the responsibility of the Town and from the Property Line into the home is the responsibility of the owner. Unfortunately, this is the most expensive solution.

## Slide 13: Summary
The Town of Braintree is currently in compliance with the lead and copper rule
The Town continues to achieve its treatment goals for the prevention of lead and copper in our drinking water
Public information regarding lead and copper including this slide show is available on the Town Website

## Slide 14: Lead Service Line Inventory
The Lead Service Inventory Process, explained
Results of the Inventory
    Total Services: 12,180
    Non-Lead Services: 5878 – 48% of the system
    Lead Services: 3448 – 28% of the system
    Galvanized Services: 40 - less than 1% of the system
    Unknown Services: 2814 – 23% of the system.
    Demonstration of Water Service Mapper

## Slide 15: Braintree DPW’s Next Steps
      Determining and documenting the material of unknown services
      Development of a Long-Term Action Plan and identification of funding

## Slide 16: Contact: Braintree Water and Sewer Office 781-843-8097 Online Information at: https://braintreema.gov/1259/Lead-and-Copper-Rule Questions